## Slide 1
PHASE 2 • ACADEMIC PROJECT REPORT
NeuroGuardian X
AI-Powered Predictive Neuro-Cardiac Healthcare Wearable
with Autonomous Emergency Intelligence
Submitted by
BHUVAN SHARMA H V 4MC23CB010
GOWTHAM MP 4MC23CB019
VINAY H M 4MC23CB060
VINAY M 4MC23CB061
Under the Guidance of
Devaraju H B
Assistant Professor
Department of Computer Science and Business Systems (CSBS)
Notes: Good [morning/afternoon] everyone. I'm presenting Phase 2 of NeuroGuardian X, an AI-powered wearable prototype for neuro-cardiac risk monitoring and autonomous emergency response. Today I'll walk through the problem we're solving, the system architecture, our methodology, implementation progress, and the validation plan for this academic prototype. This is a Phase-2 engineering report, not a certified medical device.

## Slide 2
AGENDA
Presentation Outline
NeuroGuardian X | Phase-2 Project Review
2
1
Introduction & Problem Statement
2
Objectives & Scope
3
Proposed System Overview
4
System Architecture & Data Flow
5
Methodology & Emergency Workflow
6
Hardware & Software Stack
1
System Modules
2
Dataset & AI Models
3
Testing & Validation Plan
4
Results: Targets vs Measured
5
Limitations & Future Scope
6
Conclusion & References
Notes: Here's the roadmap for this presentation. We'll start with the problem and objectives, move through the proposed architecture and data flow, cover our methodology and emergency workflow design, then the hardware and software stack, system modules, dataset and AI model plan, our testing strategy, current results versus development targets, and close with limitations, future scope and conclusions.

## Slide 3
INTRODUCTION
Continuous, Multi-Signal Health Monitoring
NeuroGuardian X | Phase-2 Project Review
3
Wearable healthcare systems support preventive monitoring by observing physiological changes continuously, not only during clinic visits.
Heart rate, SpO2 estimation, ECG morphology, EDA, movement, temperature, pressure and location together give context on stress, exertion, falls and cardiac patterns.
NeuroGuardian X is a multi-sensor academic prototype exploring continuous monitoring from an embedded AI perspective.
Phase-2 does not build a certified diagnostic device — it designs an architecture to collect, preprocess, classify and act on synchronized signals.
HR
Heart Rate / PPG
ECG
Cardiac Rhythm
EDA
Stress / Arousal
IMU
Motion / Falls
GPS
Location
Signals fused for one integrated risk picture
Notes: Wearable devices are increasingly important because they let us watch physiological signals continuously rather than only at a checkup. No single signal tells the full story, so NeuroGuardian X fuses heart rate, ECG, EDA, motion, temperature, pressure and location. At Phase 2 our goal is an academic engineering prototype — designing the architecture, not shipping a certified medical device.

## Slide 4
THE CHALLENGE
Problem Statement
NeuroGuardian X | Phase-2 Project Review
4
Most wearable prototypes track only one or two signals — insufficient for complex events like acute stress, arrhythmia-like patterns, falls or emergencies.
A single reading is ambiguous: high heart rate may mean exercise, anxiety, fever, sensor artifact, or a cardiac issue.
A fall-like motion may be an actual collapse or just vigorous activity.
Single-threshold decisions are unreliable for safety-critical alerts.
What's Needed
A platform that continuously collects multi-sensor data, analyzes risk-relevant patterns, informs the user, and supports autonomous emergency escalation — without unsupported medical claims.
Notes: The core problem is that isolated signals are ambiguous. A raised heart rate could mean many things, and a fall-like motion could be a real emergency or just exercise. Existing single-signal or single-threshold approaches can't reliably tell these apart. NeuroGuardian X is designed to combine multi-sensor context, signal-quality checks and activity awareness to make safer, more informed alert decisions.

## Slide 5
GOALS
Project Objectives & Scope
NeuroGuardian X | Phase-2 Project Review
5
Objectives
Interface all sensors (MAX30102, AD8232, GSR/EDA, ICM-42688, temperature, BMP390, GPS, SOS, vibration) with the XIAO ESP32-S3 over BLE.
Build a synchronized acquisition pipeline with timestamps, sampling policy and signal-quality checks.
Implement preprocessing for all signal modalities.
Train/evaluate stress, ECG/rhythm and fall/activity models on public + project data.
Build a Flutter app for dashboards, alerts and emergency-contact setup.
Design a graded emergency workflow with automatic and manual (SOS) triggers.
Validate the system with appropriate metrics, separating measured results from targets.
Scope
Multi-sensor wearable around XIAO ESP32-S3
Collect & preprocess PPG, ECG, EDA, IMU, temperature, pressure, GPS, SOS data
AI + rule-assisted logic for stress, rhythm risk, fall detection, emergency escalation
Flutter app for BLE, visualization, alerts, emergency workflow
Validation via engineering metrics; unmeasured values clearly marked as targets
Notes: Our seven core objectives cover sensor interfacing, a synchronized acquisition pipeline, preprocessing, model training, the Flutter mobile app, the emergency workflow, and rigorous validation. The scope is deliberately bounded to an academic prototype: we're building and validating the engineering pipeline, and we clearly separate what's measured from what's still a development target.

## Slide 6
PROPOSED SOLUTION
Proposed System Overview
NeuroGuardian X | Phase-2 Project Review
6
NeuroGuardian X combines five subsystems into one continuous-monitoring, sensor-fusion emergency platform:
1
Wearable Sensor Node
Collects synchronized physiological, motion, environmental and emergency-input signals.
2
Embedded Processing
Sampling control, preprocessing, feature extraction, threshold checks, BLE packets, low-power operation.
3
AI / Risk Layer
Combines stress, rhythm, fall/activity, signal-quality and manual SOS signals into risk states.
4
Mobile Application
Displays live readings, stores logs, configures emergency contacts, communicates warnings.
5
Emergency Workflow
Vibration, app notification, SOS confirmation, GPS location and guardian alert logic.
Notes: The proposed system has five subsystems. The wearable sensor node captures raw signals. Embedded processing on the XIAO ESP32-S3 handles sampling, preprocessing and BLE transfer. The AI and risk layer fuses stress, rhythm, fall and SOS signals into a risk state. The Flutter mobile app displays this to the user and manages emergency contacts. Finally, the emergency workflow handles vibration, notification, confirmation and GPS-based guardian alerts.

## Slide 7
SYSTEM DESIGN
Overall System Architecture
NeuroGuardian X | Phase-2 Project Review
7
Wearable Sensor Layer
PPG, ECG, EDA, IMU, Temp, BMP390, GPS
XIAO ESP32-S3
Acquisition, filtering, BLE
Flutter Mobile App
Dashboard, alerts, consent, logs
Optional Secure Updates
Model updates & reports
On-device Risk Engine
Stress, rhythm, fall, SOS logic
Emergency Workflow
Vibration, SOS, GPS message
Features
User / guardian
Risk event
The wearable node captures signals and does first-level preprocessing; features and status packets travel over BLE to the Flutter app. The risk layer runs on-device / app-side, and emergency decisions use a combined state machine — manual SOS always has priority; automatic escalation needs high-confidence risk patterns or repeated warnings.
Notes: This is the high-level architecture. The wearable sensor layer feeds the XIAO ESP32-S3, which does acquisition and BLE transfer. Features flow into an on-device risk engine that fuses stress, rhythm, fall and SOS signals. The Flutter app is the user interface, and it connects to the emergency workflow, which handles vibration alerts, SOS confirmation and GPS-tagged guardian notification. Manual SOS always takes priority over automatic escalation.

## Slide 8
DATA FLOW
Context Diagram (DFD Level 0)
NeuroGuardian X | Phase-2 Project Review
8
User / Patient
NeuroGuardian X System
Guardian / Emergency Contact
Public Datasets +
Project Sensor Data
Alerts, vitals
Risk + GPS alert
Training data
The system sits between the user (who wears the device and receives alerts/vitals) and the guardian or emergency contact (who receives risk summaries and GPS-tagged alerts). Public datasets and project sensor recordings feed model training.
Notes: At the context level, NeuroGuardian X sits between the user, who wears the device and gets alerts, and a guardian or emergency contact, who receives risk summaries and GPS-tagged emergency messages. Public datasets like WESAD and PhysioNet, along with our own project sensor data, feed into the system as training data for the underlying models.

## Slide 9
DATA FLOW
Internal Data Flow (DFD Level 1)
NeuroGuardian X | Phase-2 Project Review
9
1. Sensor
Acquisition
2. Signal
Preprocessing
3. Feature
Extraction
4. AI
Inference
5. Risk Decision
Engine
Local Logs
raw data, windows
SOS / Emergency
Alert
critical state
Raw signals move through preprocessing, feature extraction and AI inference before reaching the risk decision engine. Intermediate data (raw samples, cleaned windows, feature scores) is logged locally; critical states trigger the SOS / emergency alert path.
Notes: Internally, sensor acquisition feeds signal preprocessing, then feature extraction, then AI inference, and finally the risk decision engine. Each stage logs data locally — raw samples, cleaned windows and feature scores — for later analysis. When the risk decision engine identifies a critical state, it triggers the SOS or emergency alert path directly.

## Slide 10
SYSTEM DESIGN
UML Use-Case Design
NeuroGuardian X | Phase-2 Project Review
10
Actor | Use Cases
User / Patient | Wear device; view live readings; receive vibration alert; press SOS; confirm/cancel emergency; review trends.
Guardian / Emergency Contact | Receive alert; view shared GPS location and risk summary; respond through configured channel.
Developer / Researcher | Collect labeled data; train models; validate sensors; update firmware/app; review logs.
NeuroGuardian X System | Acquire signals; preprocess; classify stress/rhythm/activity; detect risk; transmit BLE packets; trigger alerts.
Notes: The use-case model has four actors. The user wears the device, views readings, and can press SOS or confirm/cancel emergencies. The guardian receives alerts with GPS location and a risk summary. The developer collects data, trains models, and maintains firmware. The system itself acquires signals, classifies risk, and triggers alerts autonomously when needed.

## Slide 11
METHODOLOGY
Methodology & Activity Flow
NeuroGuardian X | Phase-2 Project Review
11
1
Initialize sensor drivers, BLE service, thresholds & saved settings
2
Check sensor availability & signal quality; flag noisy/unavailable channels
3
Collect synchronized windows (PPG, ECG, EDA, IMU, temp, pressure, GPS)
4
Preprocess data, extract features, run model / rule inference
5
Classify state: normal / warning / emergency candidate
6
Warning → vibrate + app alert + log; Emergency → confirm or auto-escalate with GPS
Notes: Our methodology follows seven ordered steps. We initialize sensors and BLE, then continuously check signal quality so noisy channels are flagged rather than trusted blindly. We collect synchronized windows across all modalities, preprocess and extract features, run inference, and classify the state as normal, warning or emergency candidate. Warnings trigger vibration and app alerts; emergencies go through confirmation or automatic GPS-tagged escalation.

## Slide 12
SAFETY LOGIC
Emergency Workflow: Risk Decision Flow
NeuroGuardian X | Phase-2 Project Review
12
Continuous Sensing
raw samples
Signal-Quality Check
valid features
Model + Thresholds
Risk Decision
Normal
Log + display
Warning
Vibration + app alert
Emergency
SOS + GPS message
low
medium
high / SOS
Notes: Continuous sensing, signal-quality checks and model thresholds all feed the risk decision engine. A low risk score means normal logging and display. A medium score triggers a warning — vibration plus an app alert. A high score, or a manual SOS press, triggers the full emergency workflow: an SOS message with GPS location sent to the guardian. Manual SOS always bypasses the confidence requirement.

## Slide 13
REQUIREMENTS
Hardware Requirements
NeuroGuardian X | Phase-2 Project Review
13
Component | Interface | Purpose
XIAO ESP32-S3 | I2C, ADC, GPIO, BLE, USB | Main embedded controller: acquisition, preprocessing, BLE, alert control
MAX30102 | I2C | PPG, heart-rate trend, SpO2 estimation, pulse signal quality
AD8232 | Analog ADC + lead-off GPIO | Single-lead ECG waveform, R-peak / RR feature extraction
GSR/EDA module | Analog ADC | Skin conductance / arousal feature for stress classification
ICM-42688 (IMU) | I2C / SPI | Acceleration, gyroscope, fall / activity detection
BMP390 | I2C / SPI | Pressure & altitude trend for context and vertical movement
GPS module | UART | Location coordinates for the emergency workflow
SOS button / Vibration motor | GPIO interrupt / GPIO-PWM | Manual emergency trigger; silent haptic warning & confirmation
Notes: On the hardware side, the XIAO ESP32-S3 is our main controller. MAX30102 handles PPG and SpO2, AD8232 handles single-lead ECG, and a GSR module captures skin conductance for stress features. The ICM-42688 IMU supports fall and activity detection, BMP390 adds pressure and altitude context, and a GPS module plus SOS button and vibration motor complete the emergency-response hardware.

## Slide 14
REQUIREMENTS
Software & Technology Stack
NeuroGuardian X | Phase-2 Project Review
14
Embedded Firmware
Arduino/C++ or ESP-IDF on XIAO ESP32-S3
Mobile Application
Flutter and Dart
AI Development
Python, NumPy, SciPy, scikit-learn, TensorFlow/PyTorch
Embedded Inference
TensorFlow Lite Micro or compact rule/ML model
Data Storage
CSV/JSON locally; optional secure database/cloud
Notes: Our software stack spans embedded firmware in Arduino or ESP-IDF, a Flutter and Dart mobile application, and a Python-based AI development pipeline using scikit-learn and TensorFlow or PyTorch. For embedded inference we plan to use TensorFlow Lite Micro or a compact model, and data is stored locally as CSV or JSON with an optional secure database for larger-scale logging.

## Slide 15
IMPLEMENTATION
System Modules: Firmware & Mobile App
NeuroGuardian X | Phase-2 Project Review
15
Embedded Firmware Modules
Sensor drivers — init, sample rates, fault detection
Scheduler — sampling windows, non-blocking timing
Preprocessing — filtering, invalid-reading rejection, quality flags
Feature extraction — HR, RR/HRV, EDA, IMU impact, pressure, GPS status
BLE service — live readings, risk state, battery, alert packets
Alert state machine — normal/warning/emergency/SOS, vibration timing
Power management — duty-cycling, sleep modes
Flutter Mobile Application
BLE pairing and connection-status screen
Dashboard: HR, SpO2, ECG/rhythm state, stress, fall/activity, temp, altitude, battery, GPS
Trend graphs: HR, stress score, EDA, activity intensity
Alert screen: vibration ack, emergency countdown, cancel, SOS trigger
Emergency-contact setup with consent & test-mode warning
Data export for academic validation and model training
Notes: On the firmware side, we separate concerns into sensor drivers, a scheduler, preprocessing, feature extraction, a BLE service, an alert state machine, and power management. The Flutter app covers BLE pairing, a live dashboard, trend graphs, an alert and confirmation screen, emergency-contact setup with consent, and data export for validation and model training.

## Slide 16
DATA STRATEGY
Dataset & Preprocessing
NeuroGuardian X | Phase-2 Project Review
16
Source | Signals | Purpose
WESAD (public) | ECG, EDA, EMG, resp., accel, wrist BVP/EDA/temp/ACC | Stress & affect model development
PhysioNet / MIT-BIH | Annotated ECG, beat/rhythm labels | ECG preprocessing, R-peak & rhythm model dev.
Own NeuroGuardian data | MAX30102, AD8232, GSR, IMU, temp, BMP390, GPS, SOS | Hardware validation, calibration, final testing
Preprocessing Pipeline (per modality)
PPG: DC-drift removal, motion-artifact rejection, bandpass, beat detection
ECG: bandpass + notch filtering, baseline-wander removal, R-peak detection
EDA: low-pass filter, per-user calibration, tonic/phasic separation
IMU / Temp / GPS: calibration, windowing, smoothing, fix-quality filtering
Train / Validation / Test Strategy
Subject-independent split (no participant overlap between train/test)
Public data: leave-one-subject-out or grouped splits
Project data: ~70% subjects train / 15% validation / 15% test
Notes: We combine two public datasets — WESAD for stress and affect, and PhysioNet's MIT-BIH database for ECG rhythm work — with our own NeuroGuardian sensor recordings, which are required for hardware-specific validation. Each modality has a tailored preprocessing pipeline, and we use subject-independent splits throughout so that no participant appears in both training and test sets, which keeps our performance estimates honest.

## Slide 17
INTELLIGENCE LAYER
Algorithms / Models Used
NeuroGuardian X | Phase-2 Project Review
17
Model | Inputs | Output | Metrics
Stress Classifier | HR/HRV, EDA, temp trend, motion, PPG quality | Stress level (baseline→high) or binary | Accuracy, precision, recall, F1
ECG / Rhythm Analysis | Filtered ECG, RR intervals, R-peak quality, HRV | Normal-like / brady-tachy / irregular / noisy | Sensitivity, specificity, F1, HR MAE
Fall / Activity Detector | Accel, gyro, altitude trend, post-impact inactivity | Rest / walk / run / fall-like / recovery | Accuracy, fall recall, false alerts/hr
Risk Engine | Model scores, thresholds, signal quality, SOS, GPS | Normal / warning / emergency candidate / sent | Latency, alert precision/recall
Candidate Algorithms
Interpretable baselines first: logistic regression, random forest, gradient boosting, SVM on engineered features
Then evaluate 1D CNN / LSTM / GRU / temporal convolution for ECG & time-series windows
For embedded deployment: compact feature-based models or TensorFlow-Lite-Micro-compatible networks
Notes: We plan four model types: a stress classifier using HR, HRV, EDA and motion features; an ECG/rhythm analysis model built on filtered ECG and RR intervals; a fall/activity detector using IMU and altitude signals; and a risk engine that fuses all model scores with thresholds, signal quality and SOS input. We'll start with interpretable baselines like logistic regression and random forest, then move to CNN or LSTM architectures, favoring compact models suitable for embedded deployment.

## Slide 18
QUALITY ASSURANCE
Testing & Validation Plan
NeuroGuardian X | Phase-2 Project Review
18
Test | Method | Metric / Target
Heart rate | MAX30102 vs reference ECG/chest strap | MAE/RMSE; target ±2-5 BPM at rest
Estimated SpO2 | vs reference pulse oximeter | MAE/RMSE in %; reported as estimate, not diagnosis
ECG R-peaks | AD8232 vs annotated/reference ECG | Sensitivity, PPV, RR interval error
IMU fall/activity | Controlled activity & safe fall-like tests | Fall recall, specificity, false alerts/hr
Emergency workflow | Simulated SOS & risk-event test cases | Alert latency, BLE reliability, GPS success
Software & Integration Testing
Unit tests for preprocessing & feature extraction on known sample signals
BLE packet tests: field names, units, timestamp order, reconnection
End-to-end tests: simulated high-risk input → vibration → app warning → emergency message
Notes: Sensor validation compares each channel against a reference instrument — for example heart rate against a chest strap, ECG R-peaks against annotated recordings, and fall detection against controlled activity tests. On the software side we run unit tests on preprocessing, BLE packet-level tests, and full end-to-end tests that simulate a high-risk event and verify it produces vibration, an app warning, and an emergency message.

## Slide 19
CURRENT STATUS
Results: Development Targets vs Measured
NeuroGuardian X | Phase-2 Project Review
19
At Phase-2, the architecture, hardware selection, software layers, dataset plan and validation methodology are complete. Controlled performance measurements have not yet been recorded in this report — values below are development targets unless marked otherwise.
Area | Status | Target / Plan
MAX30102 HR | In Progress | Target ±2-5 BPM at rest; evaluate MAE/RMSE vs reference
Estimated SpO2 | In Progress | Evaluate % error vs reference oximeter
AD8232 ECG | In Progress | Validate R-peak sensitivity/PPV & RR/HR error
Stress classification | Proposed | Train on WESAD + own labeled windows; report Accuracy/Precision/Recall/F1
Fall/activity detection | Proposed | Validate recall/specificity in controlled movement tests
Emergency workflow | Design Complete | Full end-to-end field validation pending
Notes: At this stage, the architecture and validation plan are complete, but final measured performance values are not yet available in this report — they're clearly marked as development targets rather than actual results. The emergency-workflow design is complete, while HR, SpO2, ECG, stress classification and fall detection are all still in progress or proposed, pending controlled hardware testing in the next phase.

## Slide 20
HONEST ASSESSMENT
Limitations & Risk Mitigation
NeuroGuardian X | Phase-2 Project Review
20
Key Limitations
Not a certified medical diagnostic device
Wrist PPG / SpO2 affected by motion, fit, skin factors, perfusion
Single-lead ECG needs medical validation for clinical interpretation
GSR/EDA influenced by temperature, humidity, movement, emotion
Fall detection may false-positive on sports/abrupt movement, false-negative on slow collapse
GPS may fail indoors or in dense urban areas
Public datasets differ from final hardware — own-device validation is mandatory
Risk Mitigation
Use “estimated / risk indicator / warning” language, not diagnostic claims
Multi-signal confirmation, countdown/cancel, manual SOS priority, test mode
Mechanical gasket/holder design, signal-quality flags, calibration protocol
Consent-based data collection; minimal storage; protect emergency contacts
Subject-independent splits and held-out testing to avoid model overfitting
Notes: We're transparent about limitations. This is not a certified medical device, and signals like wrist PPG, single-lead ECG and GSR are all sensitive to real-world conditions. For each limitation we have a mitigation: careful language around estimates rather than diagnoses, multi-signal confirmation with a cancel option before any emergency alert, mechanical design and calibration for better sensor contact, consent-based data handling, and subject-independent evaluation to avoid overfitting.

## Slide 21
LOOKING AHEAD
Future Scope & Conclusion
NeuroGuardian X | Phase-2 Project Review
21
Future Scope (Phase-3 Direction)
Collect a small, high-quality NeuroGuardian dataset with reference instruments
Compare model performance under subject-independent evaluation
Replace development targets with measured, validated values
Conclusion
The project is technically feasible: each sensor maps clearly to an intended function
The main challenge is trustworthy sensing under wearable conditions, not simply wiring sensors
The risk engine addresses this via signal-quality flags, activity context, model confidence and manual SOS
Phase-2 delivers a complete proposed architecture, hardware/software plan, dataset strategy and validation methodology
Notes: Looking ahead to Phase 3, the priority is collecting a small but high-quality NeuroGuardian-specific dataset with reference instruments, so we can replace development targets with real measured values under subject-independent evaluation. In conclusion, the project is technically feasible — the sensors map clearly to their functions — and the real engineering challenge is making readings trustworthy under wearable conditions, which our risk engine is designed to address.

## Slide 22
SOURCES
References
NeuroGuardian X | Phase-2 Project Review
22
[1] Analog Devices. MAX30102 High-Sensitivity Pulse Oximeter and Heart-Rate Sensor. analog.com
[2] Analog Devices. AD8232 Single-Lead Heart Rate Monitor Front End. analog.com
[3] Seeed Studio. Getting Started with XIAO ESP32-S3 Series. wiki.seeedstudio.com
[4] TDK InvenSense. ICM-42688-P 6-Axis MEMS MotionTracking Device. invensense.tdk.com
[5] Bosch Sensortec. BMP390 Pressure Sensor. bosch-sensortec.com
[6] Schmidt, P. et al. WESAD: A Multimodal Dataset for Wearable Stress and Affect Detection. ICMI, 2018.
[7] Moody, G.B. & Mark, R.G. The Impact of the MIT-BIH Arrhythmia Database. IEEE EMB, 2001.
[8] Goldberger, A.L. et al. PhysioBank, PhysioToolkit, and PhysioNet. Circulation, 2000.
[9] U.S. FDA. Pulse Oximeter Accuracy and Limitations — Safety Communication. fda.gov
[10] Flutter Documentation. docs.flutter.dev
Notes: These are the ten references cited in the project report, covering the datasheets for our sensors and controller, the WESAD and PhysioNet/MIT-BIH datasets used for model development, the FDA's guidance on pulse-oximeter limitations, and the Flutter documentation used for the mobile application.

## Slide 23
THANK YOU
Questions & Discussion
NeuroGuardian X — Phase-2 Academic Project Review — Department of CSBS
Notes: Thank you for your attention. That concludes the Phase-2 review of NeuroGuardian X. I'm happy to take any questions on the architecture, methodology, or validation plan.